December 10, 2007

First test of pixel prototype stave shown below for painting. Silicon heater in middle. Copper-kapton heaters at each end. YSH-70 side only has heaters. No heaters other side for these measurements.

IR setup is shown below

Water flow rate is 1 l/min

Test conditions summarized in table below.

File 100

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	31.08	0.94	32.4	28.3	C

A2	0.95	19.0	31.31	0.67	32.5	29.3	C

File 101

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	27.41	0.65	28.4	25.9	C

A2	0.95	19.0	27.36	0.80	28.4	23.8	C

File 102

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	24.85	0.46	25.6	23.4	C

A2	0.95	19.0	25.11	0.30	25.6	24.3	C

File 103

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	20.06	0.11	20.4	19.7	C

A2	0.95	19.0	20.11	0.12	20.5	19.7	C

Here is what I extract for the average delta T(assume 20C) vs P/A

| P/A(W/cm2) | delta T average |
| --- | --- |
| 0.64 | 11.2 |
| 0.44 | 7.4 |
| 0.28 | 5 |

And plot of result. Very nicely linear.

December 13, 2007

Have put heaters on both sides. Picture of setup is below.

Looking at K13D2U side. First heat this side only.

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	31.11	0.88	32.4	28.9	C

A2	0.95	19.0	31.02	0.51	32.1	29.3	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	27.58	0.53	28.6	26.1	C

A2	0.95	19.0	27.34	0.47	28.0	26.1	C

Yikes, deleted data for 107 but here is picture

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	25.31	0.45	26.1	24.1	C

A2	0.95	19.0	25.14	0.61	25.8	22.8	C

Now heat both sides about equally. Looking at K13D2U side

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	26.59	0.39	27.2	25.6	C

A2	0.95	19.0	26.45	0.32	27.0	25.4	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	30.23	0.68	31.4	28.3	C

A2	0.95	19.0	30.08	0.48	31.0	28.5	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	34.71	0.95	36.3	32.1	C

A2	0.95	19.0	34.32	0.81	35.6	31.5	C

Now look at the YSH-70 side with heating on both sides

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	34.40	0.97	35.9	32.5	C

A2	0.95	19.0	34.34	0.99	35.9	32.1	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	29.84	0.76	30.9	27.8	C

A2	0.95	19.0	29.90	0.56	30.8	28.1	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	26.37	0.51	27.2	25.1	C

A2	0.95	19.0	26.34	0.43	27.0	25.0	C

No difference between YSH-70 and K13D2U. See plot below.

January 15, 2008

Measure silicon heater, power to both sides as kapton heater power is varied from zero up to about same total power.

Looking at YSH70 side. Power on both sides of silicon heater

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	33.16	1.31	35.0	30.3	C

A2	0.95	19.0	33.54	0.88	35.0	31.3	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	33.13	1.21	34.9	30.6	C

A2	0.95	19.0	33.34	1.01	34.9	30.6	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	33.54	1.41	35.4	30.1	C

A2	0.95	19.0	33.91	0.92	35.3	31.4	C

Label	Emis	BG	Ave	SD	Max	Min	Unit

A1	0.95	19.0	34.17	1.16	35.8	31.4	C

A2	0.95	19.0	34.35	0.87	35.6	32.4	C

| Kapton Heater Power(W) | Silicon Average T |
| --- | --- |
| 0 | 33.35 |
| 2.2 | 33.23 |
| 4.85 | 33.73 |
| 8.64 | 34.26 |