Preparation for Valencia meeting						D. Lynn

Carl

NewDaq Capabilities

Electrical Performanc of Current Stave

Status of Construction of Stave07

Detectors

Hybrid

Bus Cable

Interfaces

Serial Power

Do we need to address Kapton vs. BeO hybrid?

Expected differences going to 10 cm stave from 6 cm stave.

Gil

Gil’s list

Comments

Need to Agree on Stave Attachment. Anatoli is working on bracket assuming “C” channel. What does LBL think of “C” channel?

Is it necessary to consider “Bridge” hybrid

Should we make statement about reduction in margin for thermal runaway between two approaches. My analytic calculation can be replaced with FEA.

Building 6 cm stave and will validate that one. What can we say about expected differences in thermal performance going to a 10 cm stave?

Is there any measurements BNL can do at low temp for LBL stave? Distortion, IR imaging, that would be useful?

Dave

Inputs of weights and services to simulation. How estimate.

Present Anatoli’s cylinders. Include LBL studies?

Present Sue’s Assembly Sequence. Installation also.

Discussion of fabrication of cylinders. Industrial fabrication.

Consideration of services included

General

Should we present assembly sequence? Include preliminary ideas for Robotic assembly?

Do we emphasize any advantages of our approach?

Do we address requirements? E.g. Flatness? Need from collaboration to agree on some preliminary specifications.

Competitors

We haven’t yet studies competition. Need to do so? How?

Other

Services/weights. Should agree. Need input for Carl (Hybrid Weight/area, Bus Cable Weight/area)