ATLAS DISK SECTOR THERMAL QC

| DATE: 9/10/03 | NAME: jswirth |
| --- | --- |
| SECTOR NUMBER: Proto 2 |  |
| FRONT VOLTAGE(V): 20.92 | BACK VOLTAGE(V): 20.62 |
| FRONT CURRENT(I): 1.19 | BACK CURRENT(I): 1.21 |
| INLET TEMPERATURE(C): 24.5 | OUTLET TEMPERATURE(C): |
| PUMP FLOW RATE(l/min): .76 | CHILLER SET POINT(C): 24.5 |
| COMMENTS: Target 4 on front corresponds to rtd which read 29.4 Target 1 on front corresponds to rtd which read 27.1 Target 1 on back corresponds to rtd over inlet side which read 25.4 |

FRONT PICTURE

BACK PICTURE