|  | ATLAS Pixel Local Supports Production Readiness Review |
| --- | --- |
| ATLAS Project Document No: | Institute Document No. | Created : 25/06/2001 | Page: 1 of 2 |
| ATL-IP-QA-0003 |  | Modified : | Rev. No .: 1 |
| Production and QC/QA Plan ATLAS Pixel Disk Sectors Abstract The production and QC/QA plan for the ATLAS Pixel disk sectors is described. |
| Prepared by: E. Anderssen, M. Gilchriese, J. Wirth | Checked by: | Approved by: |
| Distribution List |

| History of Changes |
| --- |
| Rev. No. | Date | Pages | Description of changes |

Table of Contents

1	Introduction	4

2	Production Plan	4

3	Assembly Breakdown Structure(ABS)	4

4	Documentation	5

5	ATLAS Part Numbers	5

6	QC/QA Measurements	5

7	Interface to ATLAS QC/QA Database	6

# Introduction

The disk sector supports and cools pixel modules in the disk region of the ATLAS detector. Six modules are mounted on each disk sector. There are six disks in the complete ATLAS pixel detector. All disks are identical and have eight sectors. There are 48 disk sectors in the complete pixel detector. A disk sector, without modules, is shown in Figure 1.

Figure 1. A disk sector without modules.

# Production Plan

The disk sectors will be fabricated by Lawrence Berkeley National Laboratory. Raw materials are supplied by external vendors.

# Assembly Breakdown Structure(ABS)

The assembly breakdown structure for the disk sector is given below

# Documentation

Drawings and specifications documents will be associated with the ABS and placed on the ATLAS Engineering and Data Management System(EDMS).

# ATLAS Part Numbers

The disk sector components and assemblies have been assigned the following ATLAS part numbers

Disk Sector Parts

05000 - 05099			Carbon-carbon plates

05100 - 05299			Aluminum tubes

05300 - 05599			Faceplates

Note that all other disk sector parts will NOT have ATLAS part identifiers.

Bare Disk Sector Assemblies

09000 - 09999			Sector assemblies

# QC/QA Measurements

Quality control(QC) measurements on the disk sector components and assemblies will be made during the procurement of parts, fabrication of parts and assembly of the disk sectors. Quality assurance will consist primarily of independent checking of the QC measurements as recorded and by repeating selected measurements on a sample basis. Individual travellers(identified by the ATLAS part number) will be associated with the major components - carbon-carbon plates, aluminum tubes and faceplates. An individual traveller will also be maintained for the assembly and final QC testing of each sector. Batch travellers will be used for other components and materials - adhesives, strain relief pieces, hardpoints,...all components that do not have an ATLAS part identifier.

The measurements to be performed are summarized in the table below. Travellers for the vendor-supplied carbon-carbon sheets, the faceplates cut from these sheets, the aluminum tubes and for the sector assembly are appended to this document. These travellers define and record the measurements to be performed and recorded.

| Test name | Attribute name | * - mandatory o - optional | Units | Data type |
| --- | --- | --- | --- | --- |
| SectorCC | CCThickness | * | mm | Float |
|  | CCDensity | * | g/cm3 | Float |
|  | (All measurements of carbon-carbon plates) |  |  | data file |
| SectorAlTube | (All measurements of aluminium tubes) |  |  | data file |
| SectorWeight | Weight (of final sector) | * | g | float |
| SectorGeom | Planarity (after parylene coating) | * | (m | float |
|  | Thickness (after parylene coating) | * | mm | float |
| SectorConduct | DeltaTFront* | * | °C | float |
|  | DeltaTBack** | * | °C | float |
|  | (Thermal performance) |  |  | image files |
| SectorSurvey | (Survey of sector coordinate system) |  |  | data file |
| SectorQC | (All measurements of assembled sectors) |  |  | data file |

The thermal performance of each sector will be measured using Pt-on-kapton heaters brought into contact with the sector faces by a vacuum fixture. This procedure has been demonstrated on prototypes, and cross-correlated with heaters rigidly afixed to the faceplates.

The tests outlined above are, of course, non-destructive tests. In addition, we plan to perform potentially destructive tests on a sample basis. These tests will include measurements of thermal performance after thermal cycling(50 times between 20oC and -35oC), thermal shock(from 20oC to -35oC in less than 60 seconds) and pressure fault conditions(8 bar absolute for one hour) followed by irradiation of sample sectors to 50 Mrad, followed by remeasurements of thermal performance. The sample size will be about 10% of the number of sectors fabricated.

# Interface to ATLAS QC/QA Database

The QC/QA measurements to be performed on the disk sector components and disk sector assemblies that will be recorded in the ATLAS QC/QA database were described above and are also defined in a separate document.

# Footnotes

* T front = Tmax (front C-C surface) – T (cooling liquid)

** T back = Tmax (back C-C surface) – T (cooling liquid)

# Comments

Enter No

Enter No

Enter Date dd/MM/yyy

Enter Date dd/MM/yyy

Enter No

Enter text of abstract

Enter Name, Institute, E-mail

Enter Number/Title

# Endnotes

ATL-IP-MN-0003, "Production Database QA-QC Test Data", June 2001.