SUMMARY OF LAYOUT AND NAMING CONVENTIONS FOR

NTC-SIGNAL CABLE ASSEMBLIES

TYPE I   NTC Cable Assembly Schematic

Schematic of NTC cable assemblies.  Two Flex PCB assemblies are manufactured at same time, AWG36 “inner” wires are cut in middle and attached to two different PP0 terminals

Schematic of Flex PCB for NTC cables

|  | Wires | Conductor | Insulation | Manufacturer |
| --- | --- | --- | --- | --- |
| Each End | 44 tw pairs | AWG28 7-strand tin plated copper | Polyimide red/green | Raydex |
| Middle | 44 tw pairs (4 bundles) | AWG36 solid copper | PN155 red/green | MWS |

Type II Cable geography on LEMO connector:  Cable-Flex area mapping:

Connector 1: Cables 1,3 map to area LL; Cables 2,4 map to area L-

Connector 2: Cables 1,3 map to area R-; Cables 2,4 map to area RR

PP1 Pinout, FlexPCB pad assignment, and Naming Conventions for NTC Cables

| CONNECTOR 1 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Female Connector Pin Number | Pin on Flex | Lead Color | Bundle | Net name | NEW Net Name | Label PP1-Flex-NetName-PP0 |
| 15 | LL01+ | Red | LL(LT) | VPIN_1 | VPIN_LT | 15L_LL01+_Vp_LT |
| 16 | LL01 | Green | LL(LT) | VPIN_RET_1 | VPIN_RET_LT | 16L_LL01_Vpr_LT |
| 17 | LL02+ | R | LL(LT) | VISET_1 | VISET_LT | 17L_LL02+_Vi_LT |
| 18 | LL02 | G | LL(LT) | VISET_RET_1 | VISET_RET_LT | 18L_LL02_Vir_LT |
| 19 |  |  |  | Drain/Shield |  | 19L_Drain/shield |
| 37 | LL03+ | R | LL(LT) | NTC_OPTO_1 | NTC_OPTO_LT | 37L_LL03+_No_LT |
| 38 | LL03 | G | LL(LT) | NTC_OPTO_RET_1 | NTC_OPTO_RET_LT | 38L_LL03_Nor_LT |
| 39 | LL04+ | R | LL(LT) | OPTO_RST_1 | OPTO_RST_LT | 39L_LL04+Ors_LT |
| 40 | LL04 | G | LL(LT) | OPTO_RST_RET_1 | OPTO_RST_RET_LT | 40L_LL04_Orsr_LT |
| 52 | L-11+ | R | L-(LB) | Spare | Spare | 52L_L-11+_Spare |
| 53 | L-11 | G | L-(LB) | Spare | Spare | 53L_L-11_Spare |
| 2 | LL05+ | R | LL(LT) | NTC_1M | NTC_L1T | 2L_LL05+_N_L1T |
| 3 | LL05 | G | LL(LT) | NTC_RET_1M | NTC_RET_L1T | 3L_LL05_Nr_L1T |
| 4 | LL06+ | R | LL(LT) | NTC_2M | NTC_L2T | 4L_LL06+_N_L2T |
| 5 | LL06 | G | LL(LT) | NTC_RET_2M | NTC_RET_L2T | 5L_LL06_Nr_L2T |
| 6 |  |  |  | Drain/Shield |  | 6L_Drain/shield |
| 27 | LL07+ | R | LL(LT) | NTC_3M | NTC_L3T | 27L_LL07+_N_L3T |
| 28 | LL07 | G | LL(LT) | NTC_RET_3M | NTC_RET_L3T | 28L_LL07_Nr_L3T |
| 29 | LL08+ | R | LL(LT) | NTC_4M | NTC_L4T | 29L_LL08+_N_L4T |
| 30 | LL08 | G | LL(LT) | NTC_RET_4M | NTC_RET_L4T | 30L_LL08_Nr_L4T |
| 31 | LL09+ | R | LL(LT) | NTC_5M | NTC_L5T | 31L_LL09+_N_L5T |
| 48 | LL09 | G | LL(LT) | NTC_RET_5M | NTC_RET_L5T | 48L_LL09_Nr_L5T |
| 46 | LL10+ | R | LL(LT) | NTC_6M | NTC_L6T | 46L_LL10+_N_L6T |
| 47 | LL10 | G | LL(LT) | NTC_RET_6M | NTC_RET_L6T | 47L_LL10_Nr_L6T |
| 59 | LL11+ | R | LL(LT) | NTC_7M | NTC_L7T | 59L_LL11+_N_L7T |
| 60 | LL11 | G | LL(LT) | NTC_RET_7M | NTC_RET_L7T | 60L_LL11_Nr_L7T |
| 20 |  |  |  | Drain/Shield |  | 20L_Drain/shield |
| 21 | L-01+ | R | L-(LB) | VPIN_2 | VPIN_LB | 21L_L-01+_Vp_LB |
| 22 | L-01 | G | L-(LB) | VPIN_RET_2 | VPIN_RET_LB | 22L_L-01_Vpr_LB |
| 23 | L-02+ | R | L-(LB) | VISET_2 | VISET_LB | 23L_L-02+_Vi_LB |
| 24 | L-02 | G | L-(LB) | VISET_RET_2 | VISET_RET_LB | 24L_L-02_Vir_LB |
| 25 | L-03+ | R | L-(LB) | NTC_OPTO_2 | NTC_OPTO_LB | 25L_L-03+_No_LB |
| 26 | L-03 | G | L-(LB) | NTC_OPTO_RET_2 | NTC_OPTO_RET_LB | 26L_L-03_Nor_LB |
| 41 | L-04+ | R | L-(LB) | OPTO_RST_2 | OPTO_RST_LB | 41L_L-04+Ors_LB |
| 42 | L-04 | G | L-(LB) | OPTO_RST_RET_2 | OPTO_RST_RET_LB | 42L_L-04_Orsr_LB |
| 7 |  |  |  | Drain/Shield |  | 7L_Drain/shield |
| 10 | L-05+ | R | L-(LB) | NTC_8M | NTC_L1B | 10L_L-05+_N_L1B |
| 11 | L-05 | G | L-(LB) | NTC_RET_8M | NTC_RET_L1B | 11L_L-05_Nr_L1B |
| 12 | L-06+ | R | L-(LB) | NTC_9M | NTC_L2B | 12L_L-06+_N_L2B |
| 13 | L-06 | G | L-(LB) | NTC_RET_9M | NTC_RET_L2B | 13L_L-06_Nr_L2B |
| 32 | L-07+ | R | L-(LB) | NTC_10M | NTC_L3B | 32L_L-07+_N_L3B |
| 33 | L-07 | G | L-(LB) | NTC_RET_10M | NTC_RET_L3B | 33L_L-07_Nr_L3B |
| 34 | L-08+ | R | L-(LB) | NTC_11M | NTC_L4B | 34L_L-08+_N_L4B |
| 35 | L-08 | G | L-(LB) | NTC_RET_11M | NTC_RET_L4B | 35L_L-08_Nr_L4B |
| 49 | L-09+ | R | L-(LB) | NTC_12M | NTC_L5B | 49L_L-09+_N_L5B |
| 50 | L-09 | G | L-(LB) | NTC_RET_12M | NTC_RET_L5B | 50L_L-09_Nr_L5B |
| 51 | L-10+ | R | L-(LB) | NTC_13M | NTC_L6B | 51L_L-10+_N_L6B |
| 61 | L-10 | G | L-(LB) | NTC_RET_13M | NTC_RET_L6B | 61L_L-10_Nr_L6B |

| CONNECTOR 2 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Female Connector Pin Number | Pin on Flex | Lead Color | Bundle | Net name | NEW Net Name | Label PP1-Flex-NetName-PP0 |
| 15 | R-01+ | Red | R-(RT) | VPIN_3 | VPIN_RT | 15R_R-01+_Vp_RT |
| 16 | R-01 | Green | R-(RT) | VPIN_RET_3 | VPIN_RET_RT | 16R_R-01_Vpr_RT |
| 17 | R-02+ | R | R-(RT) | VISET_3 | VISET_RT | 17R_R-02+_Vi_RT |
| 18 | R-02 | G | R-(RT) | VISET_RET_3 | VISET_RET_RT | 18R_R-02_Vir_RT |
| 19 |  |  |  | Drain/Shield |  | 19R_Drain/shield |
| 37 | R-03+ | R | R-(RT) | NTC_OPTO_3 | NTC_OPTO_RT | 37R_R-03+_No_RT |
| 38 | R-03 | G | R-(RT) | NTC_OPTO_RET_3 | NTC_OPTO_RET_RT | 38R_R-03_Nor_RT |
| 39 | R-04+ | R | R-(RT) | OPTO_RST_3 | OPTO_RST_RT | 39R_R-04+Ors_RT |
| 40 | R-04 | G | R-(RT) | OPTO_RST_RET_3 | OPTO_RST_RET_RT | 40R_R-04_Orsr_RT |
| 52 | RR11+ | R | RR(RB) | spare | Spare | 52R_RR11+_Spare |
| 53 | RR11 | G | RR(RB) | spare | Spare | 53R_RR11_Spare |
| 2 | R-05+ | R | R-(RT) | NTC_1T | NTC_R1T | 2R_R-05+_N_R1T |
| 3 | R-05 | G | R-(RT) | NTC_RET_1T | NTC_RET_R1T | 3R_R-05_Nr_R1T |
| 4 | R-06+ | R | R-(RT) | NTC_2T | NTC_R2T | 4R_R-06+_N_R2T |
| 5 | R-06 | G | R-(RT) | NTC_RET_2T | NTC_RET_R2T | 5R_R-06_Nr_R2T |
| 6 |  |  |  | Drain/Shield |  | 6R_Drain/shield |
| 27 | R-07+ | R | R-(RT) | NTC_3T | NTC_R3T | 27R_R-07+_N_R3T |
| 28 | R-07 | G | R-(RT) | NTC_RET_3T | NTC_RET_R3T | 28R_R-07_Nr_R3T |
| 29 | R-08+ | R | R-(RT) | NTC_4T | NTC_R4T | 29R_R-08+_N_R4T |
| 30 | R-08 | G | R-(RT) | NTC_RET_4T | NTC_RET_R4T | 30R_R-08_Nr_R4T |
| 31 | R-09+ | R | R-(RT) | NTC_5T | NTC_R5T | 31R_R-09+_N_R5T |
| 48 | R-09 | G | R-(RT) | NTC_RET_5T | NTC_RET_R5T | 48R_R-09_Nr_R5T |
| 46 | R-10+ | R | R-(RT) | NTC_6T | NTC_R6T | 46R_R-10+_N_R6T |
| 47 | R-10 | G | R-(RT) | NTC_RET_6T | NTC_RET_R6T | 47R_R-10_Nr_R6T |
| 59 | R-11+ | R | R-(RT) | NTC_7T | NTC_R7T | 59R_R-11+_N_R7T |
| 60 | R-11 | G | R-(RT) | NTC_RET_7T | NTC_RET_R7T | 60R_R-11_Nr_R7T |
| 20 |  |  |  | Drain/Shield |  | 20R_Drain/shield |
| 21 | RR01+ | R | RR(RB) | VPIN_4 | VPIN_RB | 21R_RR01+_Vp_RB |
| 22 | RR01 | G | RR(RB) | VPIN_RET_4 | VPIN_RET_RB | 22R_RR01_Vpr_RB |
| 23 | RR02+ | R | RR(RB) | VISET_4 | VISET_RB | 23R_RR02+_Vi_RB |
| 24 | RR02 | G | RR(RB) | VISET_RET_4 | VISET_RET_RB | 24R_RR02_Vir_RB |
| 25 | RR03+ | R | RR(RB) | NTC_OPTO_4 | NTC_OPTO_RB | 25R_RR03+_No_RB |
| 26 | RR03 | G | RR(RB) | NTC_OPTO_RET_4 | NTC_OPTO_RET_RB | 26R_RR03_Nor_RB |
| 41 | RR04+ | R | RR(RB) | OPTO_RST_4 | OPTO_RST_RB | 41R_RR04+Ors_RB |
| 42 | RR04 | G | RR(RB) | OPTO_RST_RET_4 | OPTO_RST_RET_RB | 42R_RR04_Orsr_RB |
| 7 |  |  |  | Drain/Shield |  | 7R_Drain/shield |
| 10 | RR05+ | R | RR(RB) | NTC_8T | NTC_R1B | 10R_RR05+_N_R1B |
| 11 | RR05 | G | RR(RB) | NTC_RET_8T | NTC_RET_R1B | 11R_RR05_Nr_R1B |
| 12 | RR06+ | R | RR(RB) | NTC_9T | NTC_R2B | 12R_RR06+_N_R2B |
| 13 | RR06 | G | RR(RB) | NTC_RET_9T | NTC_RET_R2B | 13R_RR06_Nr_R2B |
| 32 | RR07+ | R | RR(RB) | NTC_10T | NTC_R3B | 32R_RR07+_N_R3B |
| 33 | RR07 | G | RR(RB) | NTC_RET_10T | NTC_RET_R3B | 33R_RR07_Nr_R3B |
| 34 | RR08+ | R | RR(RB) | NTC_11T | NTC_R4B | 34R_RR08+_N_R4B |
| 35 | RR08 | G | RR(RB) | NTC_RET_11T | NTC_RET_R4B | 35R_RR08_Nr_R4B |
| 49 | RR09+ | R | RR(RB) | NTC_12T | NTC_R5B | 49R_RR09+_N_R5B |
| 50 | RR09 | G | RR(RB) | NTC_RET_12T | NTC_RET_R5B | 50R_RR09_Nr_R5B |
| 51 | RR10+ | R | RR(RB) | NTC_13T | NTC_R6B | 51R_RR10+_N_R6B |
| 61 | RR10 | G | RR(RB) | NTC_RET_13T | NTC_RET_R6B | 61R_RR10_Nr_R6B |