SUMMARY OF LAYOUT AND NAMING CONVENTIONS FOR

# POWER CABLE ASSEMBLIES

TYPE I    ATLAS Power Cable Assembly

Schematic of PS (power) cable assemblies.  Two assemblies are manufactured at same time, inner wires (AWG20, 22, 30) are cut in middle and attached to different PP0’s.  Six different PCB lengths are used, corresponding to PS1-6, but pinouts are identical.

Schematic of Flex PCB for PS cables

Note:  Internal end artwork will change slightly

for production units, drawing not available at this time.

|  | Wires | Conductor | Insulation | Manufacturer |
| --- | --- | --- | --- | --- |
| Each End | 28 tw pairs 28 tw pairs | AWG26 7-strand tin plated copper AWG28 7-strand tin plated copper | Polyimide red/green Polyimide red/green | Raydex Raydex |
| Middle | 14 pb pairs 14 pb pairs 28 tw pairs | AWG20 solid copper-clad aluminum AWG22 solid copper-clad aluminum AWG30 solid copper-clad aluminum | PN155 red/green PN155 red/green PN155 red/green | MWS MWS MWS |

Connector 1:     PP1 Pinout, FlexPCB pad assignment, and Naming Conventions for PS Cables

| Female Connector Pin Number | AWG26 Power Tape Pin | AWG28 Power Sense Pin | Color | Net name | Label PP1-Flex-NetName-PP0 |
| --- | --- | --- | --- | --- | --- |
| 1 | 1A |  | R | VDD_1T | 1L - 1A - Vd - 1T |
| 2 | 1B |  | G | VDD_RET_1T | 2L - 1B - Vdr - 1T |
| 3 |  | 1a | R | VDD_sense_1T | 3L - 1a - Vds - 1T |
| 4 |  | 1b | G | VDD_retsense_1T | 4L - 1b - Vdsr - 1T |
| 5 | 2A |  | R | VDD_2T | 5L - 2A - Vd - 2T |
| 6 | 2B |  | G | VDD_RET_2T | 6L - 2B - Vdr - 2T |
| 7 |  | 2a | R | VDD_sense_2T | 7L - 2a - Vds - 2T |
| 8 |  | 2b | G | VDD_retsense_2T | 8L - 2b - Vdsr - 2T |
| 9 | 3A |  | R | VDD_3T | 9L - 3A - Vd - 3T |
| 10 | 3B |  | G | VDD_RET_3T | 10L - 3B - Vdr - 3T |
| 11 |  | 3a | R | VDD_sense_3T | 11L - 3a - Vds - 3T |
| 12 |  | 3b | G | VDD_retsense_3T | 12L - 3b - Vdsr - 3T |
| 13 |  |  |  | Drain | 13L - - Vd - drain |
| 27 | 4A |  | R | VDD_4T | 27L - 4A - Vd - 4T |
| 28 | 4B |  | G | VDD_RET_4T | 28L - 4B - Vdr - 4T |
| 29 |  | 4a | R | VDD_sense_4T | 29L - 4a - Vds - 4T |
| 30 |  | 4b | G | VDD_retsense_4T | 30L - 4b - Vdsr - 4T |
| 31 | 5A |  | R | VDD_5T | 31L - 5A - Vd - 5T |
| 32 | 5B |  | G | VDD_RET_5T | 32L - 5B - Vdr - 5T |
| 33 |  | 5a | R | VDD_sense_5T | 33L - 5a - Vds - 5T |
| 34 |  | 5b | G | VDD_retsense_5T | 34L - 5b - Vdsr - 5T |
| 46 | 6A |  | R | VDD_6T | 46L - 6A - Vd - 6T |
| 47 | 6B |  | G | VDD_RET_6T | 47L - 6B - Vdr - 6T |
| 48 |  | 6a | R | VDD_sense_6T | 48L - 6a - Vds - 6T |
| 49 |  | 6b | G | VDD_retsense_6T | 49L - 6b - Vdsr - 6T |
| 50 | 7A |  | R | VDD_7T | 50L - 7A - Vd - 7T |
| 59 | 7B |  | G | VDD_RET_7T | 59L - 7B - Vdr - 7T |
| 60 |  | 7a | R | VDD_sense_7T | 60L - 7a - Vds - 7T |
| 61 |  | 7b | G | VDD_retsense_7T | 61L - 7b - Vdsr - 7T |
| 14 |  |  |  | Drain | 14L - - Va - drain |
| 15 | 1C |  | R | VDDA_1T | 15L - 1C - Va - 1T |
| 16 | 1D |  | G | VDDA_RET_1T | 16L - 1D - Var - 1T |
| 17 |  | 1c | R | VDDA_sense_1T | 17L - 1c - Vas - 1T |
| 18 |  | 1d | G | VDDA_retsense_1T | 18L - 1d - Vasr - 1T |
| 19 | 2C |  | R | VDDA_2T | 19L - 2C - Va - 2T |
| 20 | 2D |  | G | VDDA_RET_2T | 20L - 2D - Var - 2T |
| 21 |  | 2c | R | VDDA_sense_2T | 21L - 2c - Vas - 2T |
| 22 |  | 2d | G | VDDA_retsense_2T | 22L - 2d - Vasr - 2T |
| 23 | 3C |  | R | VDDA_3T | 23L - 3C - Va - 3T |
| 24 | 3D |  | G | VDDA_RET_3T | 24L - 3D - Var - 3T |
| 25 |  | 3c | R | VDDA_sense_3T | 25L - 3c - Vas - 3T |
| 26 |  | 3d | G | VDDA_retsense_3T | 26L - 3d - Vasr - 3T |
| 38 | 4C |  | R | VDDA_4T | 38L - 4C - Va - 4T |
| 39 | 4D |  | G | VDDA_RET_4T | 39L - 4D - Var - 4T |
| 40 |  | 4c | R | VDDA_sense_4T | 40L - 4c - Vas - 4T |
| 41 |  | 4d | G | VDDA_retsense_4T | 41L - 4d - Vasr - 4T |
| 42 | 5C |  | R | VDDA_5T | 42L - 5C - Va - 5T |
| 43 | 5D |  | G | VDDA_RET_5T | 43L - 5D - Var - 5T |
| 44 |  | 5c | R | VDDA_sense_5T | 44L - 5c - Vas - 5T |
| 45 |  | 5d | G | VDDA_retsense_5T | 45L - 5d - Vasr - 5T |
| 54 | 6C |  | R | VDDA_6T | 54L - 6C - Va - 6T |
| 55 | 6D |  | G | VDDA_RET_6T | 55L - 6D - Var - 6T |
| 56 |  | 6c | R | VDDA_sense_6T | 56L - 6c - Vas - 6T |
| 57 |  | 6d | G | VDDA_retsense_6T | 57L - 6d - Vasr - 6T |
| 53 | 7C |  | R | VDDA_7T | 53L - 7C - Va - 7T |
| 62 | 7D |  | G | VDDA_RET_7T | 62L - 7D - Var - 7T |
| 63 |  | 7c | R | VDDA_sense_7T | 63L - 7c - Vas - 7T |
| 64 |  | 7d | G | VDDA_retsense_7T | 64L - 7d - Vasr - 7T |
| 35 | 8A |  | R | VVDC_T | 35L - 8A - Vc - T |
| 36 |  |  |  | Drain | 36L - - Vc - drain |
| 37 | 8B |  | G | VVDC_RET_T | 37L - 8B - Vcr - T |
| 51 |  | 8a | R | VVDC_sense_T | 51L - 8a - Vcs - T |
| 52 |  | 8b | G | VVDC_retsense_T | 52L - 8b - Vcsr - T |

Connector 2:     PP1 Pinout, FlexPCB pad assignment, and Naming Conventions for PS Cables

| Female Connector Pin Number | AWG26 Power Tape Pin | AWG28 Power Sense Pin | Color | Net name | Label PP1 – Flex – Net – PP0 |
| --- | --- | --- | --- | --- | --- |
| 1 | 9A |  | R | VDD_1B | 1R - 9A - Vd - 1B |
| 2 | 9B |  | G | VDD_RET_1B | 2R - 9B - Vdr - 1B |
| 3 |  | 9a | R | VDD_sense_1B | 3R - 9a - Vds - 1B |
| 4 |  | 9b | G | VDD_retsense_1B | 4R - 9b - Vdsr - 1B |
| 5 | 10A |  | R | VDD_2B | 5R - 10A - Vd - 2B |
| 6 | 10B |  | G | VDD_RET_2B | 6R - 10B - Vdr - 2B |
| 7 |  | 10a | R | VDD_sense_2B | 7R - 10a - Vds - 2B |
| 8 |  | 10b | G | VDD_retsense_2B | 8R - 10b - Vdsr - 2B |
| 9 | 11A |  | R | VDD_3B | 9R - 11A - Vd - 3B |
| 10 | 11B |  | G | VDD_RET_3B | 10R - 11B - Vdr - 3B |
| 11 |  | 11a | R | VDD_sense_3B | 11R - 11a - Vds - 3B |
| 12 |  | 11b | G | VDD_retsense_3B | 12R - 11b - Vdsr - 3B |
| 13 |  |  |  | Drain | 13R - - Vd - drain |
| 27 | 12A |  | R | VDD_4B | 27R - 12A - Vd - 4B |
| 28 | 12B |  | G | VDD_RET_4B | 28R - 12B - Vdr - 4B |
| 29 |  | 12a | R | VDD_sense_4B | 29R - 12a - Vds - 4B |
| 30 |  | 12b | G | VDD_retsense_4B | 30R - 12b - Vdsr - 4B |
| 31 | 13A |  | R | VDD_5B | 31R - 13A - Vd - 5B |
| 32 | 13B |  | G | VDD_RET_5B | 32R - 13B - Vdr - 5B |
| 33 |  | 13a | R | VDD_sense_5B | 33R - 13a - Vds - 5B |
| 34 |  | 13b | G | VDD_retsense_5B | 34R - 13b - Vdsr - 5B |
| 46 | 14A |  | R | VDD_6B | 46R - 14A - Vd - 6B |
| 47 | 14B |  | G | VDD_RET_6B | 47R - 14B - Vdr - 6B |
| 48 |  | 14a | R | VDD_sense_6B | 48R - 14a - Vds - 6B |
| 49 |  | 14b | G | VDD_retsense_6B | 49R - 14b - Vdsr - 6B |
| 50 |  |  |  | n/c |  |
| 59 |  |  |  | n/c |  |
| 60 |  |  |  | n/c |  |
| 61 |  |  |  | n/c |  |
| 14 |  |  |  | Drain | 14R - - Va - drain |
| 15 | 9C |  | R | VDDA_1B | 15R - 9C - Va - 1B |
| 16 | 9D |  | G | VDDA_RET_1B | 16R - 9D - Var - 1B |
| 17 |  | 9c | R | VDDA_sense_1B | 17R - 9c - Vas - 1B |
| 18 |  | 9d | G | VDDA_retsense_1B | 18R - 9d - Vasr - 1B |
| 19 | 10C |  | R | VDDA_2B | 19R - 10C - Va - 2B |
| 20 | 10D |  | G | VDDA_RET_2B | 20R - 10D - Var - 2B |
| 21 |  | 10c | R | VDDA_sense_2B | 21R - 10c - Vas - 2B |
| 22 |  | 10d | G | VDDA_retsense_2B | 22R - 10d - Vasr - 2B |
| 23 | 11C |  | R | VDDA_3B | 23R - 11C - Va - 3B |
| 24 | 11D |  | G | VDDA_RET_3B | 24R - 11D - Var - 3B |
| 25 |  | 11c | R | VDDA_sense_3B | 25R - 11c - Vas - 3B |
| 26 |  | 11d | G | VDDA_retsense_3B | 26R - 11d - Vasr - 3B |
| 38 | 12C |  | R | VDDA_4B | 38R - 12C - Va - 4B |
| 39 | 12D |  | G | VDDA_RET_4B | 39R - 12D - Var - 4B |
| 40 |  | 12c | R | VDDA_sense_4B | 40R - 12c - Vas - 4B |
| 41 |  | 12d | G | VDDA_retsense_4B | 41R - 12d - Vasr - 4B |
| 42 | 13C |  | R | VDDA_5B | 42R - 13C - Va - 5B |
| 43 | 13D |  | G | VDDA_RET_5B | 43R - 13D - Var - 5B |
| 44 |  | 13c | R | VDDA_sense_5B | 44R - 13c - Vas - 5B |
| 45 |  | 13d | G | VDDA_retsense_5B | 45R - 13d - Vasr - 5B |
| 54 | 14C |  | R | VDDA_6B | 54R - 14C - Va - 6B |
| 55 | 14D |  | G | VDDA_RET_6B | 55R - 14D - Var - 6B |
| 56 |  | 14c | R | VDDA_sense_6B | 56R - 14c - Vas - 6B |
| 57 |  | 14d | G | VDDA_retsense_6B | 57R - 14d - Vasr - 6B |
| 53 |  |  |  | n/c |  |
| 62 |  |  |  | n/c |  |
| 63 |  |  |  | n/c |  |
| 64 |  |  |  | n/c |  |
| 35 | 8C |  | R | VVDC_B | 35R - 8C - Vc - B |
| 36 |  |  |  | Drain | 36R - - Vc - drain |
| 37 | 8D |  | G | VVDC_RET_B | 37R - 8D - Vcr - B |
| 51 |  | 8c | R | VVDC_sense_B | 51R - 8c - Vcs - B |
| 52 |  | 8d | G | VVDC_retsense_B | 52R - 8d - Vcsr - B |