SCT Modules on Hold or Rework or Fail

Last Update: October 7, 2003

# P001

Fixture: A1

Last step completed: IV four detectors

Reason for placing on hold: Wrong DIMS file

# P002

Fixture: A1

Last step completed: All

Reason for placing on hold: Module thickness out

# P005

Fixture: A1

Last step completed: IV four detectors

Reason for placing on hold: stereo out of spec

P009

# Fixture:

Last step completed: Testing complete

Reason for hold: Long conditioning time

# P016

Fixture: A0

Last step completed: All

Reason for placing on hold: One hybrid height out, believe was shim error

# P021

Fixture: A0

Last step completed: IV of four detectors

Reason for placing on hold: stereo deviation is 0.165.

##### P022

Fixture:

Broken

# P025

# Fixture: A2

Last step completed: IV of four detectors

Reason for placing on hold: IV on one of the detectors is very high, cannot be conditioned.

# P026

Fixture: A1

Last step completed: IV of four detectors

Reason for placing on hold: sepf is –23

# P030

Fixture: A1

Last step completed: Metrology with hybrid before wire bond

Date March 11, 2003

Reason for placing on rework:

Hyb1RightNearH deviation is 0.234 compared to 0.190mm allowable.

Hybrid edge is seen to be lifted upon visual inspection

Action taken:

Modifications to hybrid folding fixture initiated with Fred. To add screw to gently push down.

# P043

Fixture: A1

Last step completed: Glue bottom

Date March 20, 2003

Reason for placing on fail:

Substantial glue leakage through crack on topside.

Action taken:

Check of baseboard dimensions show that it is OK, well within range of previous.

Shims were remeasured and are about 9mils, which is what is calculated

X-Y metrology shows that detectors were not shifted on baseboard.

Z metrology OK

Glue pattern was investigated. Tip of dispenser is not necessarily in line with position of stage. May wander. Possible solution is to add collet to guide tip more accurately. This is in progress. Glass module was made and glue pattern measured. Location of dots nearest gap are not symmetric. One line is about .3mm closer to gap. Previous glass module measured with similar conclusion. Action is to move one of the glue lines back by 0.3mm. Another concern is that vacuum is now stronger. Combined with other issues may draw glue out of crack.

All assembly stopped. Will continue qualification of other fixtures. Will build dummy module(s) with shifted glue pattern, at least, and hopefully collet.

## P045

Fixture: A2

Last step completed: Metrology after hybrid before wire bond

Reason for placing on hold: Bond damaged during hybrid folding. Connector apparently bent back and damage both chip bonds and fanout bonds. Put in rework category.

Action taken: more care in folding.

## P049

Fixture: A2

Last step completed: Metrology with hybrid before wire bond

Reason for placing in rework: Hybrid heights out of spec.

## P058

Fixture: A5

Last step completed: IV four detectors

Reason for failure: Glue leakage in crack.

Action taken: implement additional QC on gluing. Add checks of nozzle location to through holes on baseboard and to hole and slot. Added see through plastic template to check glue pattern.

## P063

Fixture: A3

Last step completed: Full testing.

Reason for hold: High leakage current.

## P066

Fixture: A3

Last step completed: IV four detectors

Reason for hold: Stereo deviation about 0.16

P069

Fixture:

Last step completed: Testing complete

Reason for hold: IV problems

## P071

Fixture: A5

Last step completed: IV four detectors

Reason for hold: midxf –23.5. Was remeasured, msx fixed but midxf same.

P076

Fixture:

Last step completed: Hybrid partly attached

Reason for rework: hybrid not attached one end

P081

Fixture:

Last step complete: IV of 4 wafers

Reason for hold: misxf -23

## P085

Fixture: A3

Last step completed: IV four detectors

Reason for hold: midxf -13.

### P086

Fixture: A5

Last step completed: IV four detectors

Reason for hold: Missing shim on backside, glue leakage through gap.

## P089

Fixture: A3

Last step completed: IV four detectors

Reason for hold: mhx 59. Response: eventually A3 out of service.

P093

Fixture:

Last step completed:  IV of 4 wafers

Reason for hold: stereo 0.135

P097

Fixture:

Last step completed: Testing complete

Reason for hold: IV problems

## P100

Fixture: A1

Last step completed: IV four detectors

Reason for failure: Glue leakage top. Reason unknown

## P103

Fixture: A1

Last step completed: IV four detectors

Reason for hold: mhx 42. Response. A1 out of service.

## P106

Fixture: A1

Last step completed: IV four detectors

Reason for hold: mhx and mhy outside pass. Response. A1 out of service.

P107

Fixture:

Last step completed: Testing

Reason for hold: IV problems

#### P109

Fixture: A5

Last step completed: IV four detectors

Reason for failure:  Substantial glue leakage bottom. Glue dots too large, viscosity change with new boron nitride.

Reaction: change glue dispense pressure settings

## P110

Fixture: A2

Last step completed: IV four detectors

Reason for hold:  Minor glue leakage bottom. Maybe glue dots too large, viscosity change with new boron nitride.  Metrology shows odd shape in region of glue leakage.

Reaction: change glue dispense pressure settings

P114

Fixture:

Last step completed: hybrid attach

Reason for rework: hybrid damaged in fold

### P116

Fixture: A2

Last step completed: IV four detectors

Reason for hold: Glue leakage bottom

P126

Fixture: A5

Last step completed: IV four detectors

Reason for hold: I on one detector very high

P131

Fixture: A6

Last step completed: Four wafer assembly

Reason for failure: Corner chipped off, reason unknown.

P139

Fixture: A2

Last step completed: Testing

Reason for hold: two hybrid heights front don’t pass go/no go gauge, high, need more glue

P140

Fixture: A1

Last step completed: Initial testing

Reason for hold: High leakage current at 500V, hard to condition

P141

Fixture: A3

Last step completed: IV four detectors

Reason for hold: Stereo deviation 0.138

P168

Fixture: A3

Last step completed: Hybrid attach

Reason for fail: Damage by SmartScope, BeO cracked

P170

Fixture:

Last step completed: wire bonding

Reason for hold: High current, abrasion on TL corner

P174

Fixture: A5

Last step completed: IV four detectors

Reason for hold: Current on one detector too high

P176

Fixture: A2

Last step completed: IV four detectors

Reason for hold: Current on one detector too high

P179

Fixture:

Last step completed: Testing

Reason for hold: Long conditioning decay time

P180

Fixture: A5

Last step completed: Clear metrology

Reason for fail: Very large movement of detectors one side, far outside specs

A hybrid was mounted on this by mistake

P184

Fixture:

Last step completed: testing

Reason for hold: chip in TL

P188

Fixture:

Last step: IV of 4 wafers

Reason for hold: Improper alcohol cleaning, film on top. I(V) OK

P189

Fixture: A1

Last step completed: IV of 4 wafers

Reason for hold: mhy 64

P190

Fixture:

Last step completed: IV of 4 wafers

Reason for hold: Scratch TL in region of met. Frame arm

P192

Fixture:

Last step completed: IV of 4 wafers

Reason for hold: Chip on TL

P200

Fixture:

Last step completed: Hybrid attach

Reason for hold: Chip in PA on bottom hybrid.

P201

Fixture:

Last step completed: IV of 4 wafers

Reason for hold: TR edge chip. I(V) OK after modest conditioning

P204

Fixture:

Last step completed: IV of 4 wafers

Reason for hold: mhx 88, mhy-59, A1 BB support pins reinserted at correct height