# Sector Loading Checklist		VER. 1.3			17 JUNE 2004

Sector number:________________					Date: ___________

0) Mark site to load in drawings below. Enter module number: __________

1) Sector Preparation if needed (check _____ if not needed)

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Place bare sector in aluminum carrier |  |  |
| 2 | Check that sector can jiggle slightly in carrier |  |  |
| 3 | Thread fishing line through dedicated holes. |  |  |
| 4 | UV tack fishing line & cut excess |  |  |

2) Tool setup if needed (check ____ if not needed)

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Add shims to smart scope holder |  |  |
| 2 | Load tool base & secure with clamp |  |  |
| 3 | Check all screws ready (back out set screws) |  |  |
| 4 | Completely remove tube clamps from sector |  |  |
| 5 | Remove plastic covers if necessary |  |  |
| 6 | Screw sector to tooling base |  |  |
| 7 | Check that sector lays flat by gently tapping |  |  |
| 8 | Insert tape shim to lock sector in place |  |  |
| 9 | Add tool head |  |  |
| 10 | Secure cables of modules already loaded |  |  |
| 11 | Remove x2 lens from smartscope objective |  |  |
| 12 | Focus on sector face & check pipe clearance |  |  |

PAGE 2/3

Sector Number:_____________ Module Number:_____________	 Date:_____________

3) Loading setup

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Inspect target site on sector |  |  |
| 2 | Back out tool head adjustment screws |  |  |
| 3 | Place glass slide on target site, load vacuum chuck, and adjust cups to match slide. |  |  |
| 4 | Make sure tool head position is OK for new module to clear existing modules. Lock head in place. Remove chuck and glass slide. |  |  |
| 5 | Load and run smartscope program (find sector holes) |  |  |
| 6 | Make sure module in frame has been weighed |  |  |
| 7 | Place module frame on vacuum base & turn on |  |  |
| 8 | Remove all tape from cable and stick elsewhere on frame (out of the way. Do not discard). Tape cable to table |  |  |
| 9 | Cut ends of flex close to module |  |  |

3) Place module- 2 person operation.

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Make sure sector frame cable clamp is off and path for cable is clear |  |  |
| 2 | Place vacuum pickup chuck on module & switch vacuum on |  |  |
| 3 | Release module base vacuum and transfer module to sector tool |  |  |
| 4 | Secure cables with tape. Leave clamp off. |  |  |
| 5 | Check visually that module lays flat on sector. If not, adjust cup positions and try again. |  |  |
| 6 | Align |  |  |
| 7 | Lock tool head and check all 4 alignment marks with main camera. |  |  |
| 8 | Transfer chuck with module back to vacuum base. Leave chuck vacuum on and turn on base vacuum as well. |  |  |

PAGE 3/3

Sector Number:_____________ Module Number:_____________	Date:_____________

4) Glue application

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Mix new batch of glue |  |  |
| 2 | Adjust air to 16 drops / minute |  |  |
| 3 | Place 8 drops between 2 glass slides with ends offset. Cure on hot plate and shear test. |  |  |
| 4 | Apply glue on sector. Dispense three drops each hole on the external lines of the tool and four on the two inside lines. |  |  |
| 5 | Place few drops of glue on glass slide and save |  |  |

5) Place module on glue. 2 person operation

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Check that cable path is clear |  |  |
| 2 | Turn off base vacuum only and transfer module to loading tool |  |  |
| 3 | Tape down cable. Do not clamp. |  |  |
| 4 | Re-align as needed. Lock tool head. |  |  |
| 5 | Visually inspect planarity. Adjust only if a large deviation is seen. |  |  |
| 6 | Exit smartscope program and re-run, finding the sector holes again. Verify the module position. If it is off there is a problem with the fixture setup. Check that everything is tight before re-aligning. |  |  |
| 7 | Weigh empty frame with all original tape |  |  |

6) Vacuum chuck release

| Step | Action | Check | Comments |
| --- | --- | --- | --- |
| 1 | Check that glue on glass slide has set |  |  |
| 2 | UV-tack cable to sector face |  |  |
| 3 | Epoxy cable to sector face around UV tack (don’t need to wait for epoxy to cure) |  |  |
| 4 | Turn off chuck vacuum and remove chuck |  |  |
| 5 | Ad cable clamp if another module is not being loaded right away |  |  |