# ATLAS Team Trip Report

# Lawrence Berkeley National Laboratory

June 2000

| Name of Traveler | Dates of Travel | Destination(s) |
| --- | --- | --- |
| Eric Anderssen | June 10-June 21, 2000 | CERN, Geneva, Switzerland |
| Kevin Einsweiler | June 11-June 22, 2000 | CERN, Geneva, Switzerland |
| Murdock Gilchriese | June 10-June 21, 2000 | CERN, Geneva, Switzerland |
| Emanuele Mandelli | June 14-June 22, 2000 | CERN, Geneva, Switzerland |
| Roberto Marchesini | June 12-June 22, 2000 | CERN, Geneva, Switzerland |
| John Richardson | June 10-June 21, 2000 | CERN, Geneva, Switzerland |
| Tom Weber | June 10-June 21, 2000 | CERN, Geneva, Switzerland |
| Jon Wirth | June 10-June 21, 2000 | CERN, Geneva, Switzerland |

### Purpose of Trip: Attend technical meetings of the ATLAS Detector Collaboration and test equipment with facilities at CERN.

### Summary: The design, status and schedule of the technical components of the ATLAS detector and systems were evaluated at a series of technical meetings at CERN. LBNL personnel participated in and made presentations at meetings related to the Pixel Detector Subsystem, participated in design reviews and tested prototypes made at LBNL using CERN facilities.

### Costs:

## Background and Purpose

Lawrence Berkeley National Laboratory (LBNL) is a member of ATLAS Collaboration building the ATLAS detector at the Large Hadron Collider at CERN in Geneva, Switzerland. LBNL is responsible for aspects of the preparation of physics simulation tools and analysis, software development for data acquisition and data analysis, the design, development and fabrication of the Pixel Detector Subsystem and the design, development and fabrication of Semiconductor Tracker Subsystem.

Technical and other meetings are held regularly at CERN or at other locations as specified on page 1 to evaluate the design, status, schedule and cost of the software development, of the components of the Pixel Detector Subsystem and of the Semiconductor Subsystem. In addition, laboratory measurements of components of the Pixel Detector Subsystem and of the Semiconductor Tracker Subsystem are made at CERN in collaboration with physicists and engineers from the other collaborating institutions within the ATLAS Collaboration. Measurements of the performance of prototype and final components of the Pixel Detector and Semiconductor Tracker are also made in or near charged particle beams at CERN.

## Activities

### Pixel Detector Subsystem

A one week meeting of the ATLAS pixel collaborating institutions was held to discuss in detail the technical status and near-term plans and schedules for the Pixel Detector Subsystem. Future budgets and projected costs were also discussed. The status of electronics, mechanics, silicon sensors, services, test beam analysis, software for track reconstruction and interfaces to other systems were evaluated in detail. A Final Design Review of the ATLAS Pixel Mechanics Local Supports was held. An internal design review of the evaporative cooling system for the Pixel System was held. Pixel assemblies were tested in the H8 test beam.

## Roles

Eric Anderssen

Mr. Anderssen is the lead engineer at LBNL for the US work on the mechanics of the pixel detector. He also has the responsibility for integrating the pixel detector services and participated in and made presentations at meetings on this subject. He made presentations at the ATLAS Final Design Review of the Pixel Mechanics Local supports. He participated in an internal review of the ATLAS Inner Detector cooling system. He also participated in the tests of mechanical prototypes made at LBNL in the evaporative cooling facility at CERN.

Kevin Einsweiler

Dr. Einsweiler is the Electronics Coordinator for the ATLAS Pixel Project. He led and made a number of presentations in meetings on the integrated circuit electronics for the Pixel Detector, the off-detector electronics and the power supplies. Detailed design meetings were held by him on the design of the next prototype of the integrated circuits needed for the Pixel Detector. Schedules and plans were developed with European collaborators. He participated in other Pixel Detector meetings. He presented the status and proposed plan for electronics development to the Pixel Detector Steering Group. He organized an led a multi-day design workshop on the next prototype pixel IC.

Murdock Gilchriese

He participated in  Pixel Detector meetings and in the Pixel Detector Steering Group meeting. He made a presentation on the LBNL pixel mechanics at the ATLAS Final Design Review of the Pixel Mechanics Local Supports. He participated in an internal review of the ATLAS Inner Detector cooling system. He also participated in the tests of mechanical prototypes made at LBNL in the evaporative cooling facility at CERN.

Emanuele Mandelli

He presented his work on the design of the pixel front-end integrated circuit to the pixel electronics group. He took part in the design workshop on the next prototype IC organized by Dr. Einsweiler.

Roberto Marchesini

He presented his work on the design of the pixel front-end integrated circuit to the pixel electronics group. He took part in the design workshop on the next prototype IC organized by Dr. Einsweiler.

John Richardson

Dr. Richardson presented test results obtained by him at LBNL on measurements of the pixel prototype integrated circuits and related assemblies. He also coordinated test of pixel assemblies in the CERN H8 test beam.

Tom Weber

Mr. Weber transported part of the prototypes of the pixel mechanical structure made at LBNL. He assembled these prototypes at CERN and enabled them to be tested with the evaporative cooling facility at CERN. He participated in the lengthy test program for these prototypes. He dismantled the equipment after the tests and transported part of it back to LBNL.

Jon Wirth

Mr. Wirth transported part of the prototypes of the pixel mechanical structure made at LBNL. He assembled these prototypes at CERN and enabled them to be tested with the evaporative cooling facility at CERN. He participated in the lengthy test program for these prototypes. He dismantled the equipment after the tests and transported part of it back to LBNL.

## Recommendations

## No changes in LBNL responsibilities within the ATLAS Collaboration resulted from these meetings and no impact on current DoE planning is foreseen.

## Appendix I

### Itinerary

| Traveler | Departure Point | Departure Date | Arrival Date | Arrival Point |
| --- | --- | --- | --- | --- |
| Eric Anderssen | San Francisco | June 10, 2000 | June 11, 2000 | Geneva, Switzerland |
| Kevin Einsweiler | San Francisco | June 11, 2000 | June 12, 2000 | Geneva, Switzerland |
| Murdock Gilchriese | San Francisco | June 10, 2000 | June 11, 2000 | Geneva, Switzerland |
| Emanuele Mandelli | Milano, Italy | June 14, 2000 | June 14, 2000 | Geneva, Switzerland |
| Roberto Marchesini | San Francisco | June 12, 2000 | June 13, 2000 | Geneva, Switzerland |
| John Richardson | San Francisco | June 10, 2000 | June 11, 2000 | Geneva, Switzerland |
| Tom Weber | San Francisco | June 10, 2000 | June 11, 2000 | Geneva, Switzerland |
| Jon Wirth | San Francisco | June 10, 2000 | June 11, 2000 | Geneva, Switzerland |

### Persons Contacted

The ATLAS Collaboration is very large - approximately 150 institutions and 1500 physicists. It is not possible to list here all of the persons contacted during ATLAS meetings.

### Literature

Minutes and copies of the presentations given at ATLAS meetings are available electronically from the ATLAS Web site